PBOT Library Manual rev00
by Efren S. Cruzat II

Table of Contents

# Introduction

# The Hardware

For wall and line detection, the input is logic high if reflection is sensed by its sensors.

Battery inputs are scaled through a voltage divider with 12Vbatt equivalent to 2.5Vpin. A 2.5V analog reference must be used. <To be supported in the future>

# Using the Library
The library “Pbot“ must be copied to “Arduinoxxxx\libraries“.
Sample applications are provided when you open the Arduino IDE at “File>Examples>PBot“

In order to start using the library, we must follow the following procedure...

Include the header file
#include <PBot.h>

Create PBot Object
PBotClass ObjectName;

Initialize PBot Object

Without Telemetry and D-Protocol
ObjectName.begin(PBOT_TYPE,OBSTACLE,LINE);

With Telemetry or D-Protocol
ObjectName.begin(PBOT_TYPE,OBSTACLE,LINE,TELEMETRY_EN,BAUD);

PBOT	TYPE	Types or PBot applications
 SUMO	- for sumo robot applications
 LINETRACKING	- for line following/tracking mobot
 MICROMOUSE	- for micromouse
 REMOTECONTROL	- remote control robot through serial or BT
 WHEELBALANCE	- wheel balancing robot
 VACUUMCLEANER	- roomba like vacuum cleaner

OBSTACLE/LINE	Define active logics of sensors
WHITE	- detect white lines on black surface
white walls or obstacle(use WHITE always)
BLACK	- detect black lines on white surface
black walls

TELEMETRY	Enable continous reporting of sensor status
1. - disabled
2. - enabled

BAUD	Telemetry or D-Protocol Baudrate
PBOT uses Arduino TX and RX, pin 0 and 1

Sample Code

//==================================================
// MyPBot.ino
//==================================================
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK,1,9600);
// Sumo Robot Mode,
        // Detect White Obstacles,
        // Detect Black Lines
        // Telemetry Enabled
        // 9600bps baudrate

}

void loop()
{
MyPBot.moveForward(255);
}

//==================================================

# Basic Functions
## moveForward()

Description
Command the mobot to move forward at set speed

Syntax
moveForward(Speed)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Constants FULLSPEED, HIGHSPEED, MIDSPEED, LOWSPEED may be used

Returns
None

Example

#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.moveForward(FULLSPEED);
}

## moveBackward()

Description
Command the mobot to move backward at set speed

Syntax
moveBackward(Speed)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Constants FULLSPEED, HIGHSPEED, MIDSPEED, LOWSPEED may be used

Returns
None

Example

#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.moveBackward(FULLSPEED);
}

## turnLeft()

Description
Command the mobot to turn left at set speed. Speed refers to the ratio between the right motor (running at full_speed forward) and the left motor (forward speed = full_speed – Speed).

Syntax
turnLeft(Speed)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Constants FULLSPEED, HIGHSPEED, MIDSPEED, LOWSPEED may be used

Returns
None

Example
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.turnLeft(FULLSPEED);
}

## turnRight()

Description
Command the mobot to turn right at set speed. Speed refers to the ratio between the left motor (running at full_speed forward) and the right motor (forward speed = full_speed – Speed).

Syntax
turnRight(Speed)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Constants FULLSPEED, HIGHSPEED, MIDSPEED, LOWSPEED may be used

Returns
None

Example
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.turnRIGHT(FULLSPEED);
}

## rotateLeft()

Description
Command the mobot to rotate left at set speed. Speed refers to the ratio between the right motor (running at set Speed forward) and the left motor (running at set Speed backward).

Syntax
rotateLeft(Speed)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Constants FULLSPEED, HIGHSPEED, MIDSPEED, LOWSPEED may be used

Returns
None

Example
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.rotateLeft(FULLSPEED);
}

## rotateRight()

Description
Command the mobot to rotate right at set speed. Speed refers to the ratio between the left motor (running at set Speed forward) and the right motor (running at set Speed backward).

Syntax
rotateRight(Speed)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Constants FULLSPEED, HIGHSPEED, MIDSPEED, LOWSPEED may be used

Returns
None

Example
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.rotateRIGHT(FULLSPEED);
}

## stopMotors()

Description
Stop the left and right motor s.
Syntax
stopMotors()

Parameters
None

Returns
None

Example
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
MyPBot.moveForward(FULLSPEED);
delay(5000);
MyPBot.stopMotors();
}

## detectObstacle()

Description

Syntax
WallState = detectObstacle()

Parameters
None

Returns
Returns a constant of int type representing the detected wall state...

NO_OBSTACLE,
OBJECT_LEFT,
OBJECT_LEFTCENTER,
OBJECT_RIGHT,
OBJECT_RIGHTCENTER,
OBJECT_FARFRONT,
OBJECT_NEARFRONT,
OBJECT_BOTHSIDES

Example
//==================================================
// Incomplete Sumo Robot
//==================================================
#include <PBot.h>

PBotClass MyPBot;

void setup()
{
MyPBot.begin(SUMO,WHITE,BLACK);
}

void loop()
{
if(NO_OBSTACLE == MyPBot.detectObstacle())
{
MyPBot.moveForward(FULLSPEED);	// attack enemies
}
else
{
MyPBot.moveForward(LOWSPEED);	// run at min speed // to conserve power
}
if(NO_LINE != MyPBot.detectLine())
{
MyPBot.stopMotors();	// stop at bounderies
}
}

## detectLine()

Description

Syntax
LineState = detectLine()

Parameters
None

Returns
Returns a constant of int type representing the detected line state...

NO_LINE,
LINE_LEFT,
LINE_LEFTCENTER,
LINE_RIGHT,
LINE_RIGHTCENTER,
OVER_LINE,
LINE_CENTER,
LINE_FRONT

Example
//==================================================
// Simple Line Following Mobot
//==================================================
#include <PBot.h>

PBotClass MyPBot;

int	LineState;

void setup()
{
MyPBot.begin(LINETRACKING,WHITE,BLACK);
}

void loop()
{
LineState = MyPBot.detectLine()

if(LINE_LEFT == LineState)
{
MyPBot.turnLEFT(MIDSPEED);	// turn left
}
else if(LINE_RIGHT == LineState)
{
MyPBot.turnLEFT(MIDSPEED);	// turn right
}
else
{
MyPBot.moveFORWARD(FULLSPEED);	// continue forward
}
}

# Low Level Functions

## runRightMotor()

Description

Syntax
runRightMotor(Speed, Direction)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Direction: either FORWARD or REVERSE

Returns
None

Example

## runLeftMotor()

Description

Syntax
runLeftMotor(Speed, Direction)

Parameters
Speed: motor speed between 0 (off) to 255 (full speed)
Direction: either FORWARD or REVERSE

Returns
None

Example

## stopRightMotor()

Description

Syntax
stopRightMotor()

Parameters
None

Returns
None

Example

## stopLeftMotor()

Description

Syntax
stopLeftMotor()

Parameters
None

Returns
None

Example

## pollWallSensors()

Description

Syntax
pollWallSensors(&ObstacleSensorPolarity)

Parameters
boolean

Returns
None

Example

## pollLineSensors()

Description

Syntax
pollLineSensors(&LineSensorPolarity)

Parameters
boolean

Returns
None

Example

# Advanced Functions

  1. D-Protocol

    1. Command Structure

"Dxx [Command_Code] [Parameter1] [Parameter2] <Return><Line Feed>"
(At least 10mS Transmission interval)

"# This is a comment"
Comments (preceeded by a character '#')

    - Running at 9600bps / 4800bps baudrate.
    - Every packet must start with ascii character 'D' (0x44) to indicate the start of a D-Protocol packet.
    - xx is the device/module number.
    - Each string of the D-Protocol packet is preceeded by the ascii <SPACE> character 0x20. This includes the last string of the packet.
    - The Command_Code is a fixed length(4 characters) string which tells what register to access
    - There may be cases that a specific command code requires supporting parameters, these are optional depending on the command used.
    - Parameters are limited to maximum of 6 characters only. No limit on the minimum number of characters for the parameter.
    - D-Protocol command is terminated by a return (0x0D) and line feed (0x0A) characters.

    1. Protocol Table

Type	Command	Command Code	Parameter 1	Parameter 2
Low Level
	runRightMotor	rRMT	Speed / 0 - 255	Direction / 'F' - forward / 'R' - reverse
	runLeftMotor	rLMT	Speed / 0 - 255	Direction / 'F' - forward / 'R' - reverse
	stopRightMotor	sRMT	<none>	<none>
	stopLeftMotor	sLMT	<none>	<none>
High Level
	moveForward	mFWD	Speed / 0 - 255	<none>
	moveBackward	mBCK	Speed / 0 - 255	<none>
	turnLeft	tLFT	Speed / 0 - 255	<none>
	turnRight	tRGT	Speed / 0 - 255	<none>
	rotateLeft	rLFT	Speed / 0 - 255	<none>
	rotateRight	rRGT	Speed / 0 - 255	<none>
	stopMotors	sPBT	Speed / 0 - 255	<none>
Servo
	setServoAngle	sSVA	Angle / 0 - 180	<none>
	incrementServoAngle	iSVA	<none>	<none>
	decrementServoAngle	dSVA	<none>	<none>
Telemetry
	readWallSensorsCommand	rWSC	<none>	<none>
	WallSensorsReadReply	rWSR	State1 / NONE / LEFT / LEFT / RIGHT / RIGHT / FAR / NEAR	State2 / <none> / <none> / CENTER / <none> / CENTER / FRONT / FRONT
	readLineSensorsCommand	rLSC	<none>	<none>
	LineSensorsReadReply	rLSR	State1 / NONE / LEFT / LEFT / RIGHT / RIGHT / LINE / LINE	State2 / <none> / <none> / CENTER / <none> / CENTER / REAR / FRONT
Batt Voltage
	readBattStatusCommand	rBTC	<none>	<none>
	BattStatusReply	rBTR	Voltage / (xx.xxV)
Custom	(rCMx - even: command, odd: reply)
	readCustomParamCommand	rCM0	<option>	<option>
	CustomParamReply	rCM1	<option>	<option>
Unsupported
	CommandNotSupported	cNSP	NOT	KNOWN

  1. Telemetry

## void pollSensors(unsigned long ulPollingInterval);

## void reportWallSensors(void);

## void reportLineSensors(void);

  1. Remote Control

## void parseIncomingBytes(void);

## void interpretDProtocolCommands(void);

## void resetDProtocol(void);

# Future Updates

## unsigned long getRightTachoPeriod(boolean blActiveEdge);

## unsigned long getLeftTachoPeriod(boolean blActiveEdge);